## Slide 1: Biomedical Radar for Future Pervasive Healthcare Monitoring
Prof. Jenshan Lin
University of Florida
Gainesville, Florida, USA

## Slide 2: Earliest Research Report
Rabbit
Human
10 GHz CW
10 mW
30 cm
Respiratory movement
Detect amplitude variation
J. C. Lin, J. Salinger, "Microwave measurement of respiration,” IEEE MTT-S Int. Microwave Symp. Dig., pp. 285-287, 12- 14 May 1975.
J. C. Lin, "Noninvasive Microwave Measurement of Respiration," Proceedings of the IEEE, vol. 63, no. 10, p. 1530, Oct. 1975.

## Slide 3: First Non-Contact Vital Sign Sensor Chip
0.25 µm BiCMOS
3.75 mm x 3.75 mm
1.6 GHz transmitted
Direct-conversion RX
Free-running VCO
TX power = 6.5 dBm
A. D. Droitcour, O. Boric-Lubecke, V. Lubecke, J. Lin, “0.25m CMOS and BiCMOS Single Chip Direct Conversion Doppler Radars for Remote Sensing of Vital Signs,” IEEE International Solid State Circuits Conference Digest of Technical Papers, pp. 348-349, 2002.
Free-running VCO. No PLL.

## Slide 4: Different Types of Vital Sign Radar
Continuous-Wave (CW) – unmodulated
Frequency-Modulated Continuous-Wave (FMCW)
Pulsed Radar (e.g., UWB Radar)
Possible to use more complex waveforms

## Slide 5: Portable Vital Sign Radars @ UF

## Slide 6: Applications
Search & Rescue
Sleep Apnea Monitoring
Baby Monitor SIDS Prevention
Veterinary Medicine
Fitness Equipment

## Slide 7: Self-Injection-Locking Vital Sign Radar
F.-K. Wang, C.-J. Li, C.-H. Hsiao, T.-S. Horng, J. Lin, K.-C. Peng, J.-K. Jau, J.-Y. Li, and C.-C. Chen, “A novel vital-sign sensor based on a self-injection-locked oscillator,” IEEE Trans. Microw. Theory Techn., vol. 58, no. 12, pp. 4112–4120, Dec. 2010.
F.-K. Wang, T.-S. Horng, K.-C. Peng, J.-K. Jau, J.-Y. Li, and C.-C. Chen, "Single-Antenna Doppler Radars Using Self and Mutual Injection Locking for Vital Sign Detection With Random Body Movement Cancellation," IEEE Trans. Microw. Theory Techn., vol. 59, pp. 3577-3587, December 2011.

## Slide 8: Lab Animal Respiration and Heartbeat
 | Respiration | Heartbeat
Measured Rate | 0.66 Hz | 6.73 Hz
Calculated Displacement | 1.19 mm | 0.13 mm
T. Huang, J. Lin, and L. Hayward, "Non-invasive measurement of laboratory rat’s cardiorespiratory movement using a 60-GHz radar and nonlinear Doppler phase modulation,” IMWS-Bio, September 2015.

## Slide 9: Vital Sign Detection and Positioning
Y.-S. Su; C.-C. Chang; J.-J. Guo; S.-F. Chang, "2-D wireless human subjects positioning system based on respiration detections," Microwave Symposium Digest (MTT), 2012 IEEE MTT-S International , vol., no., pp.1,3, 17-22 June 2012.

## Slide 10: Future Applications
Personal Radar in smartphones
Smartphone Tricorder?
Covert Lie Detection

## Slide 11: More Future Applications
Emotion Detector – vital sensor in a phone
Sports – fitness center/gym
Vehicle/Transportation
RF Vibrometer
Gaming/Entertainment
  quiz contests, video games
  virtual reality

## Slide 12
60 GHz frequency
5 mm wavelength
0.05 - 5 meter range
180 degree field of view

## Slide 13
Through-wall measurement
walking
crawling
Y. Kim and H. Ling, "Human Activity Classification Based on Micro-Doppler Signatures Using a Support Vector Machine," in IEEE Transactions on Geoscience and Remote Sensing, vol. 47, no. 5, pp. 1328-1337, May 2009.
2.4 GHz CW radar
2-8 m
Spectrogram: Doppler Frequency vs. Time

## Slide 14
Human Marching:
One Arm Swing
Human Marching
Two-Arm Swing
M. Otero, “Application of a continuous wave radar for human gait recognition,” Proc. SPIE 5809, Signal Processing, Sensor Fusion, and Target Recognition XIV, 538 (May 31, 2005).
Y. Wang, A. E. Fathy, “Micro-Doppler signatures for intelligent human gait recognition using a UWB impulse radar,” IEEE AP-S Int. Symp. on Antennas and Propagation, July 2011.
Spectrogram: Doppler Frequency vs. Time
Human Gait Recognition
RF Biometric
Signature
RFID  Chipless RFID  Tagless RF Identification?
10 GHz CW
UWB

## Slide 15
May 12, 2008
Sichuan, China
UWB radar developed by China’s Fourth Military Medical University and manufactured by Xi’an BIKEN Hi-Tech. Development found and saved more than 10 survivors trapped in ruins.
Fcenter: 500 MHz
Range: 15 m
Penetration: 2 m brick wall
Resolution: mm

## Slide 17: Vital-bot: A vital-sign-searching robot
Wireless data link sends detected data to a remote station.
However, there are fundamental limitations:
EM wave penetration through thick layers of rubbles, especially when wet
Trade-off between penetration depth and resolution/sensitivity

## Slide 18: A Solution: Autonomous Small Robots
Fusion of emerging technologies: small radar (IC chip) + wireless power relay + energy harvesting, carried by a small robot
Wireless ad-hoc communications among robots – wireless swarm network
More effective to search survivors deep under rubbles.
A swarm of wireless-powered robotic vital-ants
Wireless power and data relayed from/to a station above ground

## Slide 19
What if, a device can sense
amplitudes, phases, and polarizations
of various frequencies in a much
wider spectrum
Electromagnetic Spectrum
Electromagnetic (EM) Eye
Applications? Impacts?
Research needed: Electronics, Antennas, Propagation (both near-field and far-field), Signal and Data Processing, …

## Slide 20
Use your imagination